## Porting

The organization of architecture-specific code in arch/$ARCH differs from one system to another.

The ARM architecture, is quite messy, in part because there is a lot of variability between the many ARM-based SoCs. Platform-dependent code is put in directories named mach-*, approximately one per SoC. There are other directories named plat-* which contain code common to several versions of an SoC. In the case of the BeagleBone Black, the relevant directory is arch/arm/mach-omap2.

Step1 – A new device tree

The board setup is controlled by the compatible property in the root node.

Each machine is defined in a structure delimited by DT_MACHINE_START and MACHINE_END macros.

The structure between DT_MACHINE_START and MACHINE_END contains a pointer to the string array which matches one of the machines in compatible property, and function pointers for the board setup functions.