### The role of Device Drivers
Kernel device driver code runs at a high privilege level, as does the rest of the kernel. It has full access to the processor address space and hardware registers. It can handle interrupts and DMA transfers. It can make use of the sophisticated kernel infrastructure for synchronization and memory management.

no policy in the kernel. It is the responsibility of user space to set the policy that governs the overall behavior of the system. For example, the loading of kernel modules in response to external events, such as plugging in a new USB device, is the responsibility of the user space program, udev, not the kernel. The kernel just supplies a means of loading a kernel module.

#### Character Devices
Character devices are identified in user space by a special file called a device node. This file name is mapped to a device driver using the major and minor numbers associated with it. Broadly speaking, the major number maps the device node to a particular device driver, and the minor number tells the driver which interface is being accessed.

 In fact, from Linux 2.6 onwards, the major number is 12 bits long, which gives valid numbers from 1 to 4,095, and the minor number is 20 bits, from 0 to 1,048,575.

When you open a character device node, the kernel checks to see whether the major and minor numbers fall into a range registered by a character device driver . If so, it passes the call to the driver, otherwise the open call fails. The device driver can extract the minor number to find out which hardware interface to use.

#### Block Devices
Block devices are also associated with a device node, which also has major and minor numbers.

Although character and block devices are identified using major and minor numbers, they are in different namespaces. A character driver with a major number 4 is in no way related to a block driver with a major number 4.

With block devices, the major number is used to identify the device driver and the minor number is used to identify the partition.

The major number for the MMC block driver is 179 (you can look it up in devices.txt). The minor numbers are used in ranges to identify different physical MMC devices, and the partitions of the storage medium that are on that device. In the case of the MMC driver, the ranges are eight minor numbers per device: the minor numbers from 0 to 7 are for the first device, the numbers from 8 to 15 are for the second, and so on. Within each range, the first minor number represents the entire device as raw sectors, and the others represent up to seven partitions. On eMMC chips, there are two 128 KiB areas of memory reserved for use by a bootloader. These are represented as devices: mmcblk1boot0 and mmcblk1boot1, and they have minor numbers 16 and 24.

SCSI disk driver, known as sd, which is used to control a range of disks that use the SCSI command set, which includes SCSI, SATA, USB mass storage, and universal flash storage (UFS). It has the major number 8 and ranges of 16 minor numbers per interface (or disk). The minor numbers from 0 to 15 are for the first interface with device nodes named sda up to sda15, the numbers from 16 to 31 are for the second disk with device nodes sdb up to sdb15, and so on. This continues up to the 16 disk from 240 to 255 with the node name sdp.

Both the MMC and SCSI block drivers expect to find a partiton table at the start of the disk. The partition table is created using utilities such as fdisk, sfidsk, or parted.

A user space program can open and interact with a block device directly via the device node. This is not a common thing to do, though, and is usually only done to perform administrative operations such as creating partitions, formatting a partition with a filesystem, and mounting. Once the filesystem is mounted, you interact with the block device indirectly through the files in that filesystem.

#### Network Devices
Network devices are not accessed through device nodes, and they do not have major and minor numbers. Instead, a network device is allocated a name by the kernel, based on a string and an instance number. Here is an example of the way a network driver registers an interface.

my_netdev = alloc_netdev(0, "net%d", NET_NAME_UNKNOWN, netdev_setup);
ret = register_netdev(my_netdev);

This creates a network device named net0 the first time it is called, net1 the second time, and so on. More common names are lo, eth0, and wlan0.

Usually, the network interface name is only used when configuring the network using utilities, such as ip and ifconfig, to establish a network address and route. Thereafter, you interact with the network driver indirectly by opening sockets, and letting the network layer decide how to route them to the right interface. However, it is possible to access network devices directly from user space by creating a socket and using the ioctl commands listed in include/linux/sockios.h.

#### Getting information from sysfs
You can define sysfs in a pedantic way as a representation of kernel objects, attributes, and relationships. A kernel object is a directory, an attribute is a file, and a relationship is a symbolic link from one object to another. From a more practical point of view, since the Linux device driver model represents all devices and drivers as kernel objects, you can see the kernel's view of the system laid out before you by looking in /sys

#### The devices: /sys/devices
This is the kernel's view of the devices discovered since boot and how they are connected to each other. It is organized at the top level by the system bus, so what you see varies from one system to another.

There are three directories that are present on all systems:
- system/: This contains devices at the heart of the system, including CPUs and clocks.
- virtual/: This contains devices that are memory-based. You will find the memory devices that appear as /dev/null, /dev/random, and /dev/zero in virtual/mem. You will find the loopback device, lo, in virtual/net.
- platform/: This is a catch-all for devices that are not connected via a conventional hardware bus. This maybe almost everything on an embedded device.

The other devices appear in directories that correspond to actual system buses. For example, the PCI root bus, if there is one, appears as pci0000:00.
#### The drivers: /sys/class
This is a view of the device drivers presented by their type. In other words, it is a software view rather than a hardware view. Each of the subdirectories represents a class of driver and is implemented by a component of the driver framework. For example, UART devices are managed by the tty layer, and you will find them in /sys/class/tty. Likewise, you will find network devices in /sys/class/net, input devices such as the keyboard, the touchscreen, and the mouse in /sys/class/input, and so on.
There is a symbolic link in each subdirectory for each instance of that type of device pointing to its representation in /sys/device.
Looking within one of these directories, we can see the attributes of the object, represented as files, and the relationships with other objects, represented by links.

The link called device points to the hardware object for the device. The link named subsystem points back to the parent subsystem, /sys/class/tty. The remaining directory entries are attributes.

Some attribute files are writable and allow you to tune parameters in the driver at runtime. The dev attribute shows the major and minor numbers of this device. This attribute is created when the driver registered this interface. It is from this file that udev and mdev find the major and minor numbers of the device driver.

#### The block drivers: /sys/block
There is one more view of the device model that is important to this discussion: the block driver view that you will find in /sys/block. There is a subdirectory for each block device.

## Device drivers in user space

These drivers fall into two broad categories: those that you control through files in sysfs, including GPIO and LEDs, and serial buses that expose a generic interface through a device node, such as I2C.

### GPIO
General-Purpose Input/Output (GPIO) is the simplest form of digital interface since it gives you direct access to individual hardware pins, each of which can be in one of two states: either high or low.
On-chip GPIO bits are routed through to GPIO pins on the chip package via a multiplexer, known as a pin mux. There maybe additional GPIO pins available off-chip in the power management chip, and in dedicated GPIO extenders, connected through I2C or SPI buses. All this diversity is handled by a kernel subsystem known as gpiolib, which is not actually a library but the infrastructure GPIO drivers use to expose I/O in a consistent way.

Applications can interact with gpiolib through files in the /sys/class/gpio directory.

# ls /sys/class/gpio
export gpiochip0 gpiochip32 gpiochip64 gpiochip96 unexport
The directories named gpiochip0 through to gpiochip96 represent four GPIO registers, each with 32 GPIO bits. If you look in one of the gpiochip directories, you will see the following:
# ls /sys/class/gpio/gpiochip96
base label ngpio power subsystem uevent
The file named base contains the number of the first GPIO pin in the register and ngpio contains the number of bits in the register. In this case, gpiochip96/base is 96 and gpiochip96/ngpio is 32, which tells you that it contains GPIO bits 96 to 127. It is possible for there to be a gap between the last GPIO in one register and the first GPIO in the next.
To control a GPIO bit from user space, you first have to export it from kernel space, which you do by writing the GPIO number to /sys/class/gpio/export. This example shows the process for GPIO 53, which is wired to user LED 0 on the BeagleBone Black:
# echo 53 > /sys/class/gpio/export
# ls /sys/class/gpio
export gpio53 gpiochip0 gpiochip32 gpiochip64 gpiochip96 unexport
Now, there is a new directory, gpio53, which contains the files you need to control the pin. If the GPIO bit is already claimed by the kernel, you will not be able to export it in this way.
The directory gpio53 contains these files:
# ls /sys/class/gpio/gpio53
active_low direction power uevent
device edge subsystem value

The pin begins as an input. To change it to an output, write out to the direction file. The file value contains the current state of the pin, which is 0 for low and 1 for high. If it is an output; you can change the state by writing 0 or 1 to value. Sometimes, the meaning of low and high is reversed in hardware, so writing 1 to active_low inverts the meaning of value such that a low voltage is reported as 1 and a high voltage as 0.
You can remove a GPIO from user space control by writing the GPIO number to/sys/class/gpio/unexport.
#### Handling interrupts from GPIO
In many cases, a GPIO input can be configured to generate an interrupt when it changes state, which allows you to wait for the interrupt rather than polling in an inefficient software loop. If the GPIO bit can generate interrupts, the file called edge exists. Initially, it has the value called none, meaning that it does not generate interrupts. To enable interrupts, you can set it to one of these values:
- rising: Interrupt on rising edge
- falling: Interrupt on falling edge
- both: Interrupt on both rising and falling edges
- none: No interrupts (default)
You can wait for an interrupt using the poll() function with POLLPRI as the event. If you want to wait for a rising edge on GPIO 48, you first enable the interrupts:
# echo 48 > /sys/class/gpio/export
# echo falling > /sys/class/gpio/gpio48/edge
Then, you use poll(2) to wait for the change.

### LEDs
LEDs are often controlled though a GPIO pin, but there is another kernel subsystem that offers more specialized control specific to the purpose. The leds kernel subsystem adds the ability to set brightness, should the LED have that ability, and it can handle LEDs connected in other ways than a simple GPIO pin. It can be configured to trigger the LED on an event such as block device access or just a heartbeat to show that the device is working. You will have to configure your kernel with the option, CONFIG_LEDS_CLASS, and with the LED trigger actions that are appropriate to you.

As with GPIOs, LEDs are controlled through an interface in sysfs in the directory /sys/class/leds. In the case of the BeagleBone Black, the names of the LEDs are encoded in the device tree in the form devicename:colour:function, as shown here:
# ls /sys/class/leds
beaglebone:green:heartbeat beaglebone:green:usr2
beaglebone:green:mmc0 beaglebone:green:usr3

# cd /sys/class/leds/beaglebone\:green\:usr2
# ls
brightness max_brightness subsystem uevent
device power trigger
The brightness file controls the brightness of the LED and can be a number between 0 (off) and max_brightness (fully on). If the LED doesn't support intermediate brightness, any non-zero value turns it on. The file called trigger lists the events that trigger the LED to turn on. The list of triggers is implementation dependent. Here is an example:
# cat trigger
none mmc0 mmc1 timer oneshot heartbeat backlight gpio [cpu0]
default-on
The trigger currently selected is shown in square brackets. You can change it by writing one of the other triggers to the file. If you want to control the LED entirely through brightness, select none. If you set the trigger to timer, two extra files appear that allow you to set the on and off times in milliseconds:
# echo timer > trigger
# ls
brightness delay_on max_brightness subsystem uevent
delay_off device power trigger
# cat delay_on
500
# cat /sys/class/leds/beaglebone:green:heartbeat/delay_off
500
If the LED has on-chip timer hardware, the blinking takes place without interrupting the CPU.
### I2C
I2C is a simple low speed 2-wire bus that is common on embedded boards, typically used to access peripherals that are not on the SoC, such as display controllers, camera sensors, GPIO extenders, and so on. There is a related standard known as system management bus (SMBus) that is found on PCs, which is used to access temperature and voltage sensors. SMBus is a subset of I2C.
I2C is a master-slave protocol with the master being one or more host controllers on the SoC. Slaves have a 7-bit address assigned by the manufacturer (read the data sheet), allowing up to 128 nodes per bus, but 16 are reserved, so only 112 nodes are allowed in practice. The master may initiate a read or write transactions with one of the slaves. Frequently, the first byte is used to specify a register on the slave, and the remaining bytes are the data read from or written to that register.
There is one device node for each host controller, for example, this SoC has four:
# ls -l /dev/i2c*
crw-rw---- 1 root i2c 89, 0 Jan 1 00:18 /dev/i2c-0
crw-rw---- 1 root i2c 89, 1 Jan 1 00:18 /dev/i2c-1
crw-rw---- 1 root i2c 89, 2 Jan 1 00:18 /dev/i2c-2
crw-rw---- 1 root i2c 89, 3 Jan 1 00:18 /dev/i2c-3
The device interface provides a series of ioctl commands that query the host controller and send the read and write commands to I2C slaves. There is a package named i2c-tools, which uses this interface to provide basic command-line tools to interact with I2C devices. The tools are as follows:
- i2cdetect: This lists the I2C adapters, and probes the bus
- i2cdump: This dumps data from all the registers of an I2C peripheral
- i2cget: This reads data from an I2C slave
- i2cset: This writes data to an I2C slave

### Serial Peripheral Interface (SPI)
The SPI bus is similar to I2C, but is a lot faster, up to tens of MHz. The interface uses four wires with separate send and receive lines, which allow it to operate in full duplex. Each chip on the bus is selected with a dedicated chip select line. It is commonly used to connect to touchscreen sensors, display controllers, and serial NOR flash devices.
As with I2C, it is a master-slave protocol with most SoCs implementing one or more master host controllers. There is a generic SPI device driver, which you can enable through the kernel configuration CONFIG_SPI_SPIDEV. It creates a device node for each SPI controller, which allows you to access SPI chips from user space. The device nodes are named spidev[bus].[chip select]:
# ls -l /dev/spi*
crw-rw---- 1 root root 153, 0 Jan 1 00:29 /dev/spidev1.0

## Writing a kernel device driver

There are other ways to communicate with device drivers than just read and write:
- ioctl: The ioctl function allows you to pass two arguments to your driver which can have any meaning you like. By convention, the first argument is a command, which selects one of several functions in your driver, and the second is a pointer to a structure, which serves as a container for the input and output parameters. This is a blank canvas that allows you to design any program interface you like. It is pretty common when the driver and application are closely linked and written by the same team. However, ioctl is deprecated in the kernel, and you will find it hard to get any drivers with new uses of ioctl accepted upstream. The kernel maintainers dislike ioctl because it makes kernel code and application code too interdependent, and it is hard to keep both of them in step across kernel versions and architectures.
- sysfs: This is the preferred way now, a good example being the GPIO interface described earlier. The advantages are that it is somewhat self-documenting, so long as you choose descriptive names for the files. It is also scriptable because the file contents are usually text strings. On the other hand, the requirement for each file to contain a single value makes it hard to achieve atomicity if you need to change more than one value at a time. Conversely, ioctl passes all its arguments in a structure in a single function call.
- mmap: You can get direct access to kernel buffers and hardware registers by mapping kernel memory into user space, bypassing the kernel. You may still need some kernel code to handle interrupts and DMA. There is a subsystem that encapsulates this idea, known as uio, which is short for user I/O. There is more documentation in Documentation/DocBook/uio-howto, and there are example drivers in drivers/uio.
- sigio: You can send a signal from a driver using the kernel function named kill_fasync() to notify applications of an event such as input becoming ready or an interrupt being received. By convention, the signal called SIGIO is used, but it could be any. You can see some examples in the UIO driver, drivers/uio/uio.c, and in the RTC driver, drivers/char/rtc.c. The main problem is that it is difficult to write reliable signal handlers in user space, and so it remains a little-used facility.
- debugfs: This is another pseudo filesystem that represents kernel data as files and directories, similar to proc and sysfs. The main distinction is that debugfs must not contain information that is needed for the normal operation of the system; it is for the debug and trace information only. It is mounted as mount -t debugfs debug /sys/kernel/debug. There is a good description of debugfs in the kernel documentation, Documentation/filesystems/debugfs.txt.
- proc: The proc filesystem is deprecated for all new code unless it relates to processes, which was the original intended purpose for the filesystem. However, you can use proc to publish any information you choose. And, unlike sysfs and debugfs, it is available to non-GPL modules.
- netlink: This is a socket protocol family. AF_NETLINK creates a socket that links kernel space to user space. It was originally created so that network tools could communicate with the Linux network code to access the routing tables and other details. It is also used by udev to pass events from the kernel to the udev daemon. It is very rarely used in general device drivers.

the macros called module_init and module_exit specify the functions to be called when the module is loaded and unloaded. The three macros named MODULE_* add some basic information about the module, which can be retrieved from the compiled kernel module using the modinfo command.

When the module is loaded, the dummy_init() function is called. You can see the point at which it becomes a character device when is makes the call to register_chrdev, passing a pointer to struct file_operations, which contains pointers to the four functions that the driver implements. While register_chrdev tells the kernel that there is a driver with a major number of 42, it doesn't say anything about the class of driver, and so it will not create an entry in /sys/class. Without an entry in /sys/class, the device manager cannot create device nodes. So, the next few lines of code create a device class, dummy and four devices of that class called dummy0 to dummy3. The result is that the /sys/class/dummy directory is created when the driver is initialized, containing subdirectories dummy0 to dummy3. Each of the subdirectories contains a file, dev, with the major and minor numbers of the device. This is all that a device manager needs to create device nodes: /dev/dummy0 to /dev/dummy3.
The dummy_exit function has to release the resources claimed by dummy_init, which here means freeing up the device class and major number.
The file operations for this driver are implemented by dummy_open(), dummy_read(), dummy_write(), and dummy_release() and are called when a user space program calls open(2), read(2), write(2), and close(2).

### Compiling kernel modules
You can copy driver code into the kernel source tree and modify makefiles to build it, or you can compile it as a module out of tree.

Building out of tree
You need a simple makefile which uses the kernel build system to do the hard work:
LINUXDIR := $(HOME)/MELP/build/linux

obj-m := dummy.o
all:
        make ARCH=arm CROSS_COMPILE=arm-cortex_a8-linux-gnueabihf- \
        -C $(LINUXDIR) M=$(shell pwd)
clean:
        make -C $(LINUXDIR) M=$(shell pwd) clean
Set LINUXDIR to the directory of the kernel for your target device that you will be running the module on. The obj-m := dummy.o code will invoke the kernel build rule to take the source file, dummy.c, and create kernel module, dummy.ko.
Kernel modules are not binary compatible between kernel releases and configurations: the module will only load on the kernel it was compiled with.

Building as in-tree module
Choose a directory appropriate to the type of driver you have. The driver is a basic character device, so I would put dummy.c in drivers/char. Then, edit the makefile in the directory, and add a line to build the driver unconditionally as a module, as follows:
obj-m += dummy.o
Or add the following line to build it unconditionally as a built-in:
obj-y += dummy.o
If you want to make the driver optional, you can add a menu option to the Kconfig file and make the compilation conditional on the configuration option.

### Loading kernel modules
You can load, unload, and list modules using the simple insmod, lsmod, and rmmod commands. Here they are shown loading the dummy driver:
# insmod /lib/modules/4.8.12-yocto-standard/kernel/drivers/dummy.ko
# lsmod
 Tainted: G
dummy 2062 0 - Live 0xbf004000 (O)
# rmmod dummy
If the module is placed in a subdirectory in /lib/modules/<kernel release> , you can create a modules dependency database using the command, depmod -a:
# depmod -a
# ls /lib/modules/4.8.12-yocto-standard
kernel modules.alias modules.dep modules.symbols
The information in the module.* files is used by the modprobe command to locate a module by name rather than the full path.

## Discovering the hardware configuration

Devices on a discoverable bus such as PCI or USB have a query mode, which returns resource requirements and a unique identifier. The kernel matches the identifier and possibly other characteristics with the device drivers, and marries them up.

However, most of the hardware blocks on an embedded board do not have such identifiers. You have to provide the information yourself in the form of a device tree or as C structures known as platform data.
In the standard driver model for Linux, device drivers register themselves with the appropriate subsystem: PCI, USB, open firmware (device tree), platform device, and so on. The registration includes an identifier and a callback function called a probe function that is called if there is a match between the ID of the hardware and the ID of the driver. For PCI and USB, the ID is based on the vendor and the product IDs of the devices; for device tree and platform devices, it is a name (an text string).

In the absence of device tree support, there is a fallback method of describing hardware using C structures, known as the platform data.
Each piece of hardware is described by struct platform_device, which has a name and a pointer to an array of resources. The type of the resource is determined by flags, which include the following:
- IORESOURCE_MEM: This is the physical address of a region of memory
- IORESOURCE_IO: This is the physical address or port number of IO registers
- IORESOURCE_IRQ: This is the interrupt number
#define VERSATILE_ETH_BASE 0x10010000
#define IRQ_ETH 25
static struct resource smc91x_resources[] = {
  [0] = {
    .start = VERSATILE_ETH_BASE,
    .end = VERSATILE_ETH_BASE + SZ_64K - 1,
    .flags = IORESOURCE_MEM,
  },
  [1] = {
    .start = IRQ_ETH,
    .end = IRQ_ETH,
    .flags = IORESOURCE_IRQ,
  },
};
static struct platform_device smc91x_device = {
  .name = "smc91x",
  .id = 0,
  .num_resources = ARRAY_SIZE(smc91x_resources),
  .resource = smc91x_resources,
};

The platform data has to be registered with the kernel, usually when the board is initialized:
void __init versatile_init(void)
{
  platform_device_register(&versatile_flash_device);
  platform_device_register(&versatile_i2c_device);
platform_device_register(&smc91x_device);
  [ ...]

### Linking hardware with device drivers
The corresponding driver code is in drivers/net/ethernet/smsc/smc91x.c, and it works with both the device tree and platform data. Here is the initialization code:
static const struct of_device_id smc91x_match[] = {
  { .compatible = "smsc,lan91c94", },
  { .compatible = "smsc,lan91c111", },
  {},
};
MODULE_DEVICE_TABLE(of, smc91x_match);
static struct platform_driver smc_driver = {
  .probe = smc_drv_probe,
  .remove = smc_drv_remove,
  .driver = {
    .name = "smc91x",
    .of_match_table = of_match_ptr(smc91x_match),
  },
};
static int __init smc_driver_init(void)
{
  return platform_driver_register(&smc_driver);
}
static void __exit smc_driver_exit(void)
{
  platform_driver_unregister(&smc_driver);
}
module_init(smc_driver_init);
module_exit(smc_driver_exit);
When the driver is initialized, it calls platform_driver_register(), pointing to struct platform_driver, in which there is a callback to a probe function, a driver name, smc91x, and a pointer to struct of_device_id.
If this driver has been configured by the device tree, the kernel will look for a match between the compatible property in the device tree node and the string pointed to by the compatible structure element. For each match, it calls the probe function.

On the other hand, if it was configured through platform data, the probe function will be called for each match on the string pointed to by driver.name.
The probe function extracts information about the interface:

static int smc_drv_probe(struct platform_device *pdev)
{
  struct smc91x_platdata *pd = dev_get_platdata(&pdev->dev);
  const struct of_device_id *match = NULL;
  struct resource *res, *ires;
  int irq;

  res = platform_get_resource(pdev, IORESOURCE_MEM, 0);
  ires = platform_get_resource(pdev, IORESOURCE_IRQ, 0);
  [...]
  addr = ioremap(res->start, SMC_IO_EXTENT);
  irq = ires->start;
  [...]
}
The calls to platform_get_resource() extract the memory and irq information from either the device tree or the platform data. It is up to the driver to map the memory and install the interrupt handler. The third parameter, which is zero in both of the previous cases, comes into play if there is more than one resource of that particular type.

The main thing to remember here is that drivers should register a probe function and enough information for the kernel to call the probe , as it finds matches with the hardware it knows about. The linkage between the hardware described by the device tree and the device driver is through the compatible property. The linkage between platform data and a driver is through the name.