Configurations to enable for debugging

~ CONFIG_BUG, CONFIG_KALLSYMS (General setup -> Configure standard kernel features)
   + CONFIG_KPROBES (General setup)
   + CONFIG_DYNAMIC_DEBUG (Kernel hacking -> printk and dmesg options)
   + CONFIG_DEBUG_INFO (Kernel hacking -> Compile-time checks and compiler options)
   ~ CONFIG_DEBUG_FS (Kernel hacking -> Compile-time checks and compiler options)
   ~ CONFIG_MAGIC_SYSRQ (Kernel hacking)
   ~ CONFIG_DEBUG_KERNEL (Kernel hacking)
   + CONFIG_DEBUG_KMEMLEAK, CONFIG_DEBUG_KMEMLEAK_EARLY_LOG_SIZE (say 4K) & CONFIG_DEBUG_KMEMLEAK_TEST (Kernel hacking -> Memory Debugging)
   ~ CONFIG_LOCKUP_DETECTOR (Kernel hacking -> Debug Lockups and Hangs)
   ~ CONFIG_DEBUG_SPINLOCK, CONFIG_DEBUG_MUTEXES (Kernel hacking -> Lock Debugging)
   + CONFIG_FUNCTION_TRACER (Kernel hacking -> Tracers)
   + CONFIG_KGDB, CONFIG_KGDB_SERIAL_CONSOLE, CONFIG_KGDB_KDB (Kernel hacking)

Gdb commands

+ l [N] - list the program from line number N, or main & then next 10 next 10
+ b thread - breakpoint on thread function
+ i[nfo] b[reakpoints] [<no>] - list the current breakpoints/watchpoints
+ r - start running the program
+ i[nfo] threads - list the existing threads
+ thread <tno> - switch to thread <tno>
+ b 15 thread 3 - breakpoint on line number 15 but only for thread 3
+ tb[reak] 15 - temporary breakpoint
+ c - continue running
+ s - step into (function) execution. (si for instr level)
+ n - step over (function) execution. (ni for instr level)
+ d[elete] <nos> - delete breakpoint/watchpoint <nos>
+ bt - backtrace - show call trace
+ enable/disable <no> - enable/disable breakpoint/watchpoint <no>
+ awatch, rwatch, watch <expr> - watch <expr> (access(r/w), read, write of variables in it)
+ display <expr> - display expr on every halt
+ i[nfo] - list all possible infos
+ i[nfo] watchpoints - list all the watchpoints
+ attach/detach - to/from a process(i.e. inferior) or file
+ set detach-on-fork off - stops (default) detaching process on fork
+ i[nfo] inferiors - list of existing process (main, child, ...)
+ inferior <ino> - switch to inferior <ino>
+ disassemble - show assembly

Debugging by printing

printk() and dmesg() uses,
int klogctl()

syslogd
#include <syslog.h>

openlog()
syslog()
closelog()

klogd – bridge between kernel ring buffer and syslogd

User Space level System logs: /var/log/*
Debugging by querying

-Through kernel windows

/proc
- process related stuff
- general systems information – cpuinfo, meminfo,
- drivers related info – devices, iomem, interrupts

/sys
-busses,class,devices

Using ioctl
-using custom commands

Crash dumping and analysis

OOPS analysis

CONFIG_BUG, CONFIG_KALLSYMS

Call Trace

Check out EIP, say 0xbf00f0f8 (and Call Trace)

Check out the (partial) address in /proc/kallsyms, e.g. 0xbf00f0f8, or 0xbf00f0f, or 0xbf00f0, ... till whichever matches first

Also note the base address of the corresponding module (page_fault), say 0xbf00f000

Note the offset, say 0xf8

$ cat /proc/kallsyms

$ objdump -d/-S <obj/exe>

> Check the offset in the output of "arm-linux-gnueabihf-objdump <options> page_fault.ko", where options could be -d or -S,

> arm-linux-gnueabihf-gdb (with l *0xf8),

 > arm-linux-gnueabihf-addr2line [-i] -e page_fault.ko 0xf8

NARROW DOWN the bug

Crash dumping
-using 2 kernels
- System kernel: CONFIG_KEXEC, CONFIG_DEBUG_INFO
- Dump-capture kernel: CONFIG_CRASH_DUMP, CONFIG_PROC_VMCORE, Other architecture specific CONFIG_s

For kexec & kdump, refer to Kernel/linux-3.12.9/Documentation/kdump/kdump.txt
Dynamic Debugging

Dynamically enabling / disabling of all calls of pr_debug(), dev_dbg(), print_hex_dump_debug(), print_hex_dump_bytes().

Debug File System's typical mount: /sys/kernel/debug (dfs).

+ Ways to control dynamic debugging:
echo "file <file> line <lno> -/+p" > <dfs>/dynamic_debug/control
echo "module <driver_name> -/+p" > <dfs>/dynamic_debug/control
echo "func <function> -/+p" > <dfs>/dynamic_debug/control
+ Format of control file: "file:line [module]function flags format"
Flags: p(r_debug), f(unction name), l(ine no), m(odule name), t(hread id)
NB print_hex_dump_debug(), print_hex_dump_bytes() uses only p
+ Try out Drivers/Debugging/dyn_debug.ko with the Apps/debug_ops
Check: grep dyn_debug /sys/kernel/debug/dynamic_debug/control
Enable all prints: echo "module dyn_debug +p" > /sys/kernel/debug/dynamic_debug/control
Or,
dyndbg==p as argument to insmod
Disable write's print: echo "file dyn_debug.c line 46 -p" > /sys/kernel/debug/dynamic_debug/control
+ Try out the controlling of the built-in code thread_builtin (optional)
Check: grep thread_builtin /sys/kernel/debug/dynamic_debug/control
Enable: echo "file thread_builtin.c line 73 +p" > /sys/kernel/debug/dynamic_debug/control
Disable: echo "file thread_builtin.c line 73 -p" > /sys/kernel/debug/dynamic_debug/control

Kernel Hacking

Soft lockups
- Spinlocks (recursive)

Memory leak

Magic SysRq:
+ Alt+SysRq <key>
+ echo <key> > /proc/sysrq-trigger
+ Ctrl-a f <key> (through minicom)

Kernel Debuggers

1. Kernel debugger frontend: (kdb)
- basic operations over serial console

For configuring over serial:
+ echo ttyO0 > /sys/module/kgdboc/parameters/kgdboc (after boot), or add "kgdboc=ttyO0,115200" to the bootargs in /boot/uboot/uEnv.txt
For configuring on monitor w/ (PS/2) kbd:
+ echo kbd > /sys/module/kgdboc/parameters/kgdboc (after boot), or add "kgdboc=kbd" to the bootargs in /boot/uboot/uEnv.txt
Activating kdb prompt:
+ Add "kgdbwait" to the bootargs in /boot/uboot/uEnv.txt (for prompt during boot up), Or
+ Press "SysRq g" (for prompt at any time)
Try kdb commands: "?/help" for complete listing (go, bt, rd, rm, lsmod, ps, dmesg, kgdb, ...).

2. kgdb
-remote debugging

-remote connection and debug through gdb vmlinux
gdb <kernel src>/vmlinux /proc/kcore

Steps for remote debugging using arm-linux-gnueabihf-gdb:
+ Type kgdb on kdb prompt of BBB (through minicom)
+ Quit minicom without reset (Ctrl + A q)
+ arm-linux-gnueabihf-gdb --tui vmlinux (from the linux-3.12.9 folder, where vmlinux was built with root privileges for accessing /dev/ttyUSB0)
+ target remote /dev/ttyUSB0 (at the gdb prompt)
Now, its all gdb.
Kernel probe