There are two sequences of events that are required to boot a Linux computer and make it usable: boot and startup.

 The boot sequence starts when the computer is turned on, and is completed when the kernel is initialized and systemd is launched.

The startup process then takes over and finishes the task of getting the Linux computer into an operational state.

Comprises of:
BIOS POST
- Boot loader (GRUB2)
- Kernel initialization
- Start systemd, the parent of all processes.

### BIOS POST
The first step of the Linux boot process really has nothing whatever to do with Linux. This is the hardware portion of the boot process and is the same for any operating system. When power is first applied to the computer it runs the POST (Power On Self Test) which is part of the BIOS (Basic I/O System).

BIOS POST checks the basic operability of the hardware and then it issues a BIOS interrupt, INT 13H, which locates the boot sectors on any attached bootable devices. The first boot sector it finds that contains a valid boot record is loaded into RAM and control is then transferred to the code that was loaded from the boot sector.

The boot sector is really the first stage of the boot loader. There are three boot loaders used by most Linux distributions, GRUB, GRUB2, and LILO.

GRUB2
GRUB2 stands for "GRand Unified Bootloader, version 2" and it is now the primary bootloader for most current Linux distributions.
GRUB has been designed to be compatible with the multiboot specification which allows GRUB to boot many versions of Linux and other free operating systems; it can also chain load the boot record of proprietary operating systems.
GRUB can also allow the user to choose to boot from among several different kernels for any given Linux distribution. This affords the ability to boot to a previous kernel version if an updated one fails somehow or is incompatible with an important piece of software. GRUB can be configured using the /boot/grub/grub.conf file.
GRUB2 is configured with /boot/grub2/grub.cfg.

The primary function of either GRUB is to get the Linux kernel loaded into memory and running. Both versions of GRUB work essentially the same way and have the same three stages:
#### Stage 1
As mentioned in the BIOS POST section, at the end of POST, BIOS searches the attached disks for a boot record, usually located in the Master Boot Record (MBR), it loads the first one it finds into memory and then starts execution of the boot record. The bootstrap code, i.e., GRUB2 stage 1, is very small because it must fit into the first 512-byte sector on the hard drive along with the partition table. The total amount of space allocated for the actual bootstrap code in a classic generic MBR is 446 bytes. The 446 Byte file for stage 1 is named boot.img and does not contain the partition table which is added to the boot record separately.
It does not understand filesystem structures. Therefore the sole purpose of stage 1 is to locate and load stage 1.5. stage 1.5 of GRUB must be located in the space between the boot record itself and the first partition on the drive. After loading GRUB stage 1.5 into RAM, stage 1 turns control over to stage 1.5.

#### Stage 1.5
stage 1.5 of GRUB must be located in the space between the boot record itself and the first partition on the disk drive. This space was left unused historically for technical reasons. The first partition on the hard drive begins at sector 63 and with the MBR in sector 0, that leaves 62 512-byte sectors—31,744 bytes—in which to store the core.img file which is stage 1.5 of GRUB. The core.img file is 25,389 Bytes so there is plenty of space available between the MBR and the first disk partition in which to store it.

Because of the larger amount of code that can be accommodated for stage 1.5, it can have enough code to contain a few common filesystem drivers, such as the standard EXT and other Linux filesystems, FAT, and NTFS. The GRUB2 core.img is much more complex and capable than the older GRUB1 stage 1.5. This means that stage 2 of GRUB2 can be located on a standard EXT filesystem but it cannot be located on a logical volume. So the standard location for the stage 2 files is in the /boot filesystem, specifically /boot/grub2.

The /boot directory must be located on a filesystem that is supported by GRUB. Not all filesystems are. The function of stage 1.5 is to begin execution with the filesystem drivers necessary to locate the stage 2 files in the /boot filesystem and load the needed drivers.

#### Stage 2
All of the files for GRUB stage 2 are located in the /boot/grub2 directory and several subdirectories. GRUB2 does not have an image file like stages 1 and 2. Instead, it consists mostly of runtime kernel modules that are loaded as needed from the /boot/grub2/i386-pc directory.

The function of GRUB2 stage 2 is to locate and load a Linux kernel into RAM and turn control of the computer over to the kernel. The kernel and its associated files are located in the /boot directory. The kernel files are identifiable as they are all named starting with vmlinuz.

GRUB2, like GRUB1, supports booting from one of a selection of Linux kernels. The Red Hat package manager, DNF, supports keeping multiple versions of the kernel so that if a problem occurs with the newest one, an older version of the kernel can be booted. By default, GRUB provides a pre-boot menu of the installed kernels, including a rescue option and, if configured, a recovery option.
Stage 2 of GRUB2 loads the selected kernel into memory and turns control of the computer over to the kernel.

Kernel

All of the kernels are in a self-extracting, compressed format to save space. The kernels are located in the /boot directory, along with an initial RAM disk image, and device maps of the hard drives.

After the selected kernel is loaded into memory and begins executing, it must first extract itself from the compressed version of the file before it can perform any useful work. Once the kernel has extracted itself, it loads systemd, which is the replacement for the old SysV init program, and turns control over to it.
This is the end of the boot process. At this point, the Linux kernel and systemd are running but unable to perform any productive tasks for the end user because nothing else is running.

## The startup process
The startup process follows the boot process and brings the Linux computer up to an operational state in which it is usable for productive work.
### systemd
systemd is the mother of all processes and it is responsible for bringing the Linux host up to a state in which productive work can be done.
Some of its functions, are to manage many aspects of a running Linux host, including mounting filesystems, and starting and managing system services required to have a productive Linux host.

First, systemd mounts the filesystems as defined by /etc/fstab, including any swap files or partitions. At this point, it can access the configuration files located in /etc, including its own. It uses its configuration file, /etc/systemd/system/default.target, to determine which state or target, into which it should boot the host.

lrwxrwxrwx 1 root root 36 Dec 6 13:42 /etc/systemd/system/default.target -> /lib/systemd/system/graphical.target

For a desktop workstation, this is typically going to be the graphical.target, which is equivalent to runlevel 5 in the old SystemV init. For a server, the default is more likely to be the multi-user.target which is like runlevel 3 in SystemV. The emergency.target is similar to single user mode.

targets and services are systemd units.

The systemd target aliases are provided by systemd for backward compatibility.
The target aliases allow scripts—and many sysadmins —to use SystemV commands like init 3 to change runlevels.
Of course, the SystemV commands are forwarded to systemd for interpretation and execution.

Each target has a set of dependencies described in its configuration file. systemd starts the required dependencies. These dependencies are the services required to run the Linux host at a specific level of functionality. When all of the dependencies listed in the target configuration files are loaded and running, the system is running at that target level.

systemd also looks at the legacy SystemV init directories to see if any startup files exist there. If so, systemd used those as configuration files to start the services described by the files.

local-fs-pre.target

        |

        v

   (various mounts and (various swap (various cryptsetup

    fsck services...) devices...) devices...) (various low-level (various low-level

        | | | services: udevd, API VFS mounts:

        v v v tmpfiles, random mqueue, configfs,

     local-fs.target swap.target cryptsetup.target seed, sysctl, ...) debugfs, ...)

        | | | | |

        \__________________|_________________ | ___________________|____________________/

        \|/

        v

        sysinit.target

        |

        ____________________________________/|\________________________________________

        / | | | \

        | | | | |

        v v | v v

        (various (various | (various rescue.service

       timers...) paths...) | sockets...) |

        | | | | v

        v v | v rescue.target

      timers.target paths.target | sockets.target

        | | | |

        v \_________________ | ___________________/

        \|/

        v

        basic.target

        |

        ____________________________________/| emergency.service

        / | | |

        | | | v

        v v v emergency.target

        display- (various system (various system

    manager.service services services)

        | required for |

        | graphical UIs) v

        | | multi-user.target

        | | |

        \_________________ | _________________/

        \|/

        v

        graphical.target

It shows the general sequence of events during systemd startup and the basic ordering requirements to ensure a successful startup.

The sysinit.target and basic.target targets can be considered as checkpoints in the startup process. Although systemd has as one of its design goals to start system services in parallel, there are still certain services and functional targets that must be started before other services and targets can be started. These checkpoints cannot be passed until all of the services and targets required by that checkpoint are fulfilled.

So the sysinit.target is reached when all of the units on which it depends are completed. All of those units, mounting filesystems, setting up swap files, starting udev, setting the random generator seed, initiating low-level services, and setting up cryptographic services if one or more filesystems are encrypted, must be completed, but within the sysinit.target those tasks can be performed in parallel.

The sysinit.target starts up all of the low-level services and units required for the system to be marginally functional and that are required to enable moving on to the basic.target.

After the sysinit.target is fulfilled, systemd next starts the basic.target, starting all of the units required to fulfill it. The basic target provides some additional functionality by starting units that re required for the next target. These include setting up things like paths to various executable directories, communication sockets, and timers.

Finally, the user-level targets, multi-user.target or graphical.target can be initialized. Notice that the multi-user.target must be reached before the graphical target dependencies can be met.

When one of these targets is reached, then startup has completed. If the multi-user.target is the default, then you should see a text mode login on the console. If graphical.target is the default, then you should see a graphical login; the specific GUI login screen you see will depend on the default display manager you use.

GRUB2 and the systemd init system are the key components in the boot and startup phases of most modern Linux distributions.

What is MBR?
A master boot record (MBR) is a special type of boot sector at the very beginning of partitioned computer mass storage devices like fixed disks or removable drives intended for use with IBM PC-compatible systems and beyond.

The MBR holds the information on how the logical partitions, containing file systems, are organized on that medium. The MBR also contains executable code to function as a loader for the installed operating system—usually by passing control over to the loader's second stage, or in conjunction with each partition's volume boot record (VBR).

The MBR consists of 512 or more bytes located in the first sector of the drive.
It may contain one or more of:
- A partition table describing the partitions of a storage device. In this context the boot sector may also be called a partition sector.
- Bootstrap code: Instructions to identify the configured bootable partition, then load and execute its volume boot record (VBR) as a chain loader.
- Optional 32-bit disk timestamp.[3]
- Optional 32-bit disk signature.[5][6][7][8]

Q) What is systemd? What are its functions?
Ans:
systemd is a software suite that provides an array of system components for Linux operating systems.
Its main aim is to unify service configuration and behavior across Linux distributions;[6] systemd's primary component is a "system and service manager"—an init system used to bootstrap user space and manage user processes. It also provides replacements for various daemons and utilities, including device management, login management, network connection management, and event logging.

systemd as unifying "pointless differences between distributions", by providing the following three general functions:[28]
- A system and service manager (manages both the system, by applying various configurations, and its services)
- A software platform (serves as a basis for developing other software)
- The glue between applications and the kernel (provides various interfaces that expose functionalities provided by the kernel)
Systemd includes features like on-demand starting of daemons, snapshot support, process tracking[29] and Inhibitor Locks.

It is not just the name of the init daemon but also refers to the entire software bundle around it, which, in addition to the systemd init daemon, includes the daemons journald, logind and networkd, and many other low-level components.

As an integrated software suite, systemd replaces the startup sequences and runlevels controlled by the traditional init daemon, along with the shell scripts executed under its control. systemd also integrates many other services that are common on Linux systems by handling user logins, the system console, device hotplugging (see udev), scheduled execution (replacing cron), logging, hostnames and locales.

systemd is the first daemon to start during booting and the last daemon to terminate during shutdown. The systemd daemon serves as the root of the user space's process tree; the first process (PID 1) has a special role on Unix systems, as it replaces the parent of a process when the original parent terminates. Therefore, the first process is particularly well suited for the purpose of monitoring daemons.

Following its integrated approach, systemd also provides replacements for various daemons and utilities, including the startup shell scripts, pm-utils, inetd, acpid, syslog, watchdog, cron and atd. systemd's core components include the following:
- systemd is a system and service manager for Linux operating systems.
- systemctl is a command to introspect and control the state of the systemd system and service manager. Not to be confused with sysctl.
- systemd-analyze may be used to determine system boot-up performance statistics and retrieve other state and tracing information from the system and service manager.

Before systemd starts

Starting up the kernel

Upon completion of its tasks, the bootloader will execute a jump to kernel code that it has loaded into main memory and begin execution, passing along any command-line options that the user has specified.

file /boot/vmlinuz indicates that it is a bzImage, meaning a big compressed one. The Linux source tree contains an extract-vmlinux tool that can be used to uncompress the file:
$# scripts/extract-vmlinux /boot/vmlinuz-$(uname -r) > vmlinux

$# file vmlinux

vmlinux: ELF 64-bit LSB executable, x86-64, version 1 (SYSV), statically

linked, stripped
The kernel is an Executable and Linking Format (ELF) binary, like Linux userspace programs. That means we can use commands from the binutils package like readelf to inspect it.

Before the main() function can run, programs need an execution context that includes heap and stack memory plus file descriptors for stdio, stdout, and stderr. Userspace programs obtain these resources from the standard library, which is glibc on most Linux systems.

ELF binaries have an interpreter, just as Bash and Python scripts do, but the interpreter need not be specified with #! as in scripts, as ELF is Linux's native format. The ELF interpreter provisions a binary with the needed resources by calling _start(), a function available from the glibc source package that can be inspected via GDB.

First install the debug package for the kernel that contains an unstripped version of vmlinux, for example apt-get install linux-image-amd64-dbg, or compile and install your own kernel from source,

gdb vmlinux followed by info files shows the ELF section init.text. List the start of program execution in init.text with l *(address), where address is the hexadecimal start of init.text. GDB will indicate that the x86_64 kernel starts up in the kernel's file arch/x86/kernel/head_64.S, where we find the assembly function start_cpu0() and code that explicitly creates a stack and decompresses the zImage before calling the x86_64 start_kernel() function. ARM 32-bit kernels have the similar arch/arm/kernel/head.S. start_kernel() is not architecture-specific, so the function lives in the kernel's init/main.c. start_kernel() is arguably Linux's true main() function.

### The kernel's hardware manifest: the device-tree and ACPI tables

At boot, the kernel needs information about the hardware beyond the processor type for which it has been compiled. The instructions in the code are augmented by configuration data that is stored separately. There are two main methods of storing this data: device-trees and ACPI tables. The kernel learns what hardware it must run at each boot by reading these files.

For embedded devices, the device-tree is a manifest of installed hardware. The device-tree is simply a file that is compiled at the same time as kernel source and is typically located in /boot alongside vmlinux.

Clearly the device-tree can be modified simply by editing the JSON-like files that compose it and rerunning the special dtc compiler that is provided with the kernel source. While the device-tree is a static file whose file path is typically passed to the kernel by the bootloader on the command line, a device-tree overlay facility has been added in recent years, where the kernel can dynamically load additional fragments in response to hotplug events after boot.

x86-family and many enterprise-grade ARM64 devices make use of the alternative Advanced Configuration and Power Interface (ACPI) mechanism. In contrast to the device-tree, the ACPI information is stored in the /sys/firmware/acpi/tables virtual filesystem that is created by the kernel at boot by accessing onboard ROM. The easy way to read the ACPI tables is with the acpidump command from the acpica-tools package.

The code in init/main.c:

The first CPU is registered with the system, global data structures are initialized, and the scheduler, interrupt handlers (IRQs), timers, and console are brought one-by-one, in strict order, online. Until the function timekeeping_init() runs, all timestamps are zero. This part of the kernel initialization is synchronous, meaning that execution occurs in precisely one thread, and no function is executed until the last one completes and returns.

The situation persists into the function rest_init(), which is called by start_kernel() at its termination.

The rather humbly named rest_init() spawns a new thread that runs kernel_init(), which invokes do_initcalls(). Users can spy on initcalls in action by appending initcall_debug to the kernel command line, resulting in dmesg entries every time an initcall function runs. initcalls pass through seven sequential levels: early, core, postcore, arch, subsys, fs, device, and late. The most user-visible part of the initcalls is the probing and setup of all the processors' peripherals: buses, network, storage, displays, etc., accompanied by the loading of their kernel modules. rest_init() also spawns a second thread on the boot processor that begins by running cpu_idle() while it waits for the scheduler to assign it work.

kernel_init() also sets up symmetric multiprocessing (SMP). With more recent kernels, find this point in dmesg output by looking for "Bringing up secondary CPUs..." SMP proceeds by "hotplugging" CPUs, meaning that it manages their lifecycle with a state machine that is notionally similar to that of devices like hotplugged USB sticks. The kernel's power-management system frequently takes individual cores offline, then wakes them as needed, so that the same CPU hotplug code is called over and over on a machine that is not busy.

the code in init/main.c is nearly finished executing when smp_init() runs: The boot processor has completed most of the one-time initialization that the other cores need not repeat. Nonetheless, the per-CPU threads must be spawned for each core to manage interrupts (IRQs), workqueues, timers, and power events on each.

Near its end, kernel_init() looks for an initrd that can execute the init process on its behalf. If it finds none, the kernel directly executes init itself.

Initrd

optionally provided to the kernel at boot is that of the initrd. The initrd often lives in /boot alongside the bzImage file vmlinuz on x86, or alongside the similar uImage and device-tree for ARM.

Distro initrd schemes contain minimal /bin, /sbin, and /etc directories along with kernel modules, plus some files in /scripts.

initrd for the most part is simply a minimal Linux root filesystem.

nearly all the executables in /bin and /sbin inside the ramdisk are symlinks to the BusyBox binary, resulting in /bin and /sbin directories that are 10x smaller than glibc's.

Why bother to create an initrd if all it does is load some modules and then start init on the regular root filesystem? Consider an encrypted root filesystem. The decryption may rely on loading a kernel module that is stored in /lib/modules on the root filesystem ... and, unsurprisingly, in the initrd as well. The crypto module could be statically compiled into the kernel instead of loaded from a file, but there are various reasons for not wanting to do so.

Unsurprisingly, storage, network, and human input device (HID) drivers may also be present in the initrd—basically any code that is not part of the kernel proper that is needed to mount the root filesystem. The initrd is also a place where users can stash their own custom ACPI table code.

initrd's are also great for testing filesystems and data-storage devices themselves. Stash these test tools in the initrd and run your tests from memory rather than from the object under test.

At last, when init runs, the system is up! Since the secondary processors are now running, the machine has become the asynchronous, preemptible, unpredictable, high-performance

All the steps in Embedded Linux Booting

(1) Software components Involved in Embedded Linux Boot Process
(a) Bootloader
(b) kernel Image
(c) root file system - either an initrd image or a NFS location
(2) Steps during Booting process of a conventional PC
(a) System Startup - PC-BIOS/BootMonitor
(b) Stage1 bootloader - MBR
(c) stage2 bootloader - LILO,GRUB etc
(d) kernel - Linux
(e) init - The User Space
(3) Booting process for an Emebedded Systems
(a) Instead of BIOS you will run program from a fixed location in Flash
(b) The components involved in the first steps of PC boot process are combined in to a single "boot strap firmware", called "boot loader".
(c) Bootloader also provides additional features useful for development & debugging.
(4) What is System Startup?
[ Exact process depends on the Target Hardware ]
(a) CPU starts exectuing BIOS at address 0xFFFF0
(b) POST (Power On Self Test) - is the first step of BIOS.
(c) run time services - involve local device enumeration and
initialization
(d) After the POST is complete, POST related code is flushed out of
memory. But BIOS runtime services remain in memory and are available to
the target OS.
(e) The runtime searches for devices that are both active and
bootable in order of preference defined in CMOS settings
(f) The primary boot loader is loaded and BIOS returns control to it
(5) The Primary boot loader
(a) Performs few optional initializations
(b) Its main job is to Load the secondary boot loader

(6) Secondary boot loader
(a) The Second Stage boot loader loads the Linux & an optional
initial RAM disk in to the memory
(b) on PC, the initrd is used as a temporary root files
system, before final root file system gets mounted. However, on embedded
systems, the initrd is generally the final root file system.
(c) The secondary loader passes control to the kernel image - kernel is
decompressed & initialized
(d) So, the secondary boot loaderis the kernel Loader, can also load optional initial RAM disk (initrd), and then invokes the kernel image
(7) Kernel Invocation
(a) As the kernel is invoked, it performs the checks on system hardware, enumerates the attached hardware devices, mounts the root device
   (b) Next it loads the necessary kernel modules
   (c) First user-space program (init) now starts and high-level system initialization is performed
   (d) The Kernel Invocation Process is similar on Embedded Linux Systems as well as on PC. We will discuss this in detail in following text.
(8) Kernel Image
   (a) Is typically a compressed image [zlib compression]
   (b) Typical named a zImage (<512 KB) or bzImage (> 512 KB)
   (c) At the head of this image (in file head.S) is a routine that does some minimal amount of hardware set up and then decompresses the kernel contained in the kernel image and places in to high memory (high memory & low memory)

PART-B

(1) Kernel Invocation Process - A Summary
(a) zImage Entry Point
(b) PERFORM BASIC HARDWARE SET UP
(c) PERFORM BASIC ENVIRONMENT SET UP (stack etc)
(d) CLEAR BSS
[Now We have set up the run time environment for the code to be
executed next]
(e) DECOMPRESS THE KERNEL IMAGE
(f) Execute the decompressed Kernel Image
- INITIALIZE PAGE TABLES
- ENABLE MMU
- DETECT CPU (& optoinal FPU) TYPE & SAVE THIS INFO
[With above set up, we are now ready to execute a general C
Code. Till now we only executed asm routines.]
(g) The First Kernel C function
- DO FURTHER INITIALIZATIONS
- LOAD INITRD
[ The above code is being executed by swapper process, the one
with pid 0]
(h) The Init Process
- FORK INIT PROCESS
- Init process is with pid 1
- Invoke Scheduler
- RELINQUISH CONTROL TO SCHEDULER
(2) zImage Entry point
(a) This is a call to the absolute physical address by boot loader
   - Refer to file arch/***/boot/compressed/head.S: start() in kernel source.
   - For the ARM process this is "arch/arm/boot/compressed/head.S: start()"
   (b) start() performs
       - basic hardware set up
       - basic environment set up
       - clears bss
       - calls the decompress_kernel()
(3) Decompressing Kernel Image
   (a) This is a call to arch/***/boot/compressed/misc.c: decompress_kernel()
       - This function decompresses the kernel image, stores it in to the RAM & returns the address of decompressed image in RAM.
   (b) on ARM processor this maps to "arch/arm/boot/compressed/misc.c: decompress_kernel()" routine.
(4) Execute the decompressed Kernel Image
   (a) After we have got the (uncompressed) kernel image in RAM, we execute it.
   (b) Execution starts with call_kernel() function call [from start()].
   (c) call_kernel() will start executing the kernel code, from Kernel
entry point.
   (d) arch/***/kernel/head.S contains the kernel entry point.
       - separate entry points for Master CPU and Secondary CPUs (for SMP
systems).
       - This code is in asm
       - Page Tables are Initialized & MMU is enabled.
       - type of CPU alongwith optional FPU is detected and stored
       - For Master CPU; start_kernel(), which is the first C function to
be executed in kernel, is called.
       - For secondary CPUs (on an SMP system); secondary_start_kernel()
is the first C function to be called.
   (e) On ARM process it maps to "arch/arm/kernel/head.S
       - Contains kernel ENTRY points for master and secondary CPU.
       - For Master CPU "mmap_switched()" is called as soon as mmu gets enabled. The mmap_switched() saves the CPU info makes a call to start_kernel()
       - For Secondary CPU "secondary_start_kernel()" is called as soon as MMU gets enabled.
(5) The first kernel C function
   (a) The start_kernel() function is being executed by the swapper process.
   (b) Refer to init/main.c: start_kernel() in the kernel source.
   (c) start_kernel():
       - a long list of initialization functions are called: this sets up interrupts, performs further memory configuration & loads the initrd.
       - calls rest_init() in the End.
   (d) econdary_start_kernel() for secondary CPUs (on SMP systems).
       - arch/***/kernel/smp.c: secondary_start_kernel()
       - for ARM, arch/arm/kernel/smp.c
       - there is not rest_init() call for secondary CPUs.
(6) Init process
   (a) Refer to init/main.c: rest_init() in kernel source.
   (b) Executed only on the Master CPU
   (c) rest_init() forks new process by calling kernel_thread() function
   (d) kernel_thread(kern_init,*,*); kern_init has PID-1
   (e) kern_init() will call the initialization scripts.
   (f) kernel_thread() defined in "arch/***/kernel/process.c: kernel_thread()".
   (g) on ARM, arch/arm/kernel/process.c
(7) Invoke scheduler
   (a) The rest_init() calls cpu_idle() in end [after it is done creating the init process]
   (b) For the Secondary CPUs (on SMP systems), cpu_idle is directly
called from secondary_start_kernel [no step-5 & hence no init process].
   (c) cpu_idle() defined in "arch/***/kernel/process.c: cpu_idle()".
   (d) on ARM, arch/arm/kernel/process.c
(8) initrd image
   (a) The initrd serves as a temporary root file system in RAM & allows the kernel to fully boot without having to mount and physical disks. Since the necessary modules needed to interface with peripherals
can be part of initrd the kernel can be very small.
   (b) pivot_root() routine: the root files system is pivoted where the initrd root file system is unmounted & the real root file system is mounted.
   (c) In any embedded system, the initrd could be the root file system.

### The Linux Boot Process
A target board booting Linux proceeds through several steps after reset to get to a system prompt. The initial steps, such as ROM startup code and register configuration, are microprocessor hardware dependent. The kernel itself contains microprocessor architecture杁ependent initialization code that is executed first. This initialization code configures the microprocessor registers for protected-mode operation and then invokes the architecture-independent kernel starting point called start_kernel. From this point on, the kernel boot process is identical for all architectures. The Linux boot process involves the following steps:
1. After a processor is reset, it executes ROM startup code.
2. The ROM startup code initializes the CPU, memory controller, and on-chip devices, and it configures the memory map. The ROM startup code then executes a bootloader.
3. The bootloader decompresses the Linux kernel into RAM from Flash memory or a TFTP server transfer. It then executes a jump to the kernel's first instruction. The kernel first configures microprocessor registers and then invokes start_kernel, which is the architecture-independent starting point.
4. The kernel initializes its caches and various hardware devices.
5. The kernel mounts the root filesystem.
6. The kernel executes the init process.
7. The executing init process loads shared runtime libraries.
8. init reads its configuration file, /etc/inittab, and executes scripts. Typically, init executes a startup script, /etc/rc.d/rcS, which configures and starts networking and other system services.
9. init enters a runlevel where system duties can be performed or the login process can start, allowing for user sessions.