Bootloaders

The job of a bootloader is to make available to a newly powered processor the resources it needs to run a general-purpose operating system like Linux.
At power-on, there not only is no virtual memory, but no DRAM until its controller is brought up.

A bootloader then turns on power supplies and scans buses and interfaces in order to locate the kernel image and the root filesystem.

Popular bootloaders like U-Boot and GRUB have support for familiar interfaces like USB, PCI, and NFS, as well as more embedded-specific devices like NOR- and NAND-flash.

Bootloaders also interact with hardware security devices like Trusted Platform Modules (TPMs) to establish a chain of trust from earliest boot.

U-Boot

The open source, widely used U-Boot bootloader is supported on systems ranging from Raspberry Pi to Nintendo devices to automotive boards to Chromebooks.

the U-Boot team offers a sandbox in which patches can be tested on the build-host, or even in a nightly Continuous Integration system.

In U-boot source folder,
$ make ARCH=sandbox defconfig

The U-Boot sandbox can even be single-stepped under the GDB debugger. Development using the sandbox is 10x faster than testing by reflashing the bootloader onto a board, and a "bricked" sandbox can be recovered with Ctrl+C.

Upon completion of its tasks, the bootloader will execute a jump to kernel code that it has loaded into main memory and begin execution, passing along any command-line options that the user has specified.