The power management system should endeavor to reduce the CPU clock frequency; during idle periods, it should choose the deepest sleep state possible; it should reduce the load by powering down unused peripherals; and it should be able to put the whole system into a suspend state.

# cat /sys/power/state

There are two approaches: external and internal.

Measuring power externally, from outside the system, we just need an ammeter to measure the current and a voltmeter to measure the voltage, and then multiply the two together in order to get the wattage. You can use basic meters that give a readout, which you then note down.

The other approach is to use the monitoring systems that are built into Linux. You will find that plenty of information is reported to you via sysfs. There is also a very useful program called PowerTOP, which gathers information together from various sources and presents it in a single place.

## Scaling the clock frequency
The power consumption of a CPU when executing code is the sum of a static component, caused by gate leakage current, among other things, and a dynamic component, caused by switching of the gates:
Pcpu = Pstatic + Pdyn
The dynamic power component is dependent on the total capacitance of the logic gates being switched, the clock frequency, and the square of the voltage:
Pdyn = CfV2
Changing the frequency by itself is not going to save any power because the same number of CPU cycles have to be completed in order to execute a given subroutine. If we reduce the frequency by half, it will take twice as long to complete the calculation, but the total power consumed due to the dynamic power component will be the same. In fact, reducing the frequency may actually increase the power budget because it takes longer for the CPU to enter an idle state. So, in these conditions, it is best to use the highest frequency possible so that the CPU can go back to idle quickly. This is called the race to idle.

There is another motivation to reduce frequency: thermal management. It may become necessary to operate at a lower frequency just to keep the temperature of the package within bounds.

Therefore, if we want to save power, we have to be able to change the voltage that the CPU core operates at. But for any given voltage, there is a maximum frequency beyond which the switching of the gates become unreliable. Higher frequencies need higher voltages, and so the two need to be adjusted together. Many SoCs implement such a feature: it is called Dynamic Voltage and Frequency Scaling, or DVFS. Manufacturers calculate optimum combinations of core frequency and voltage. Each combination is called Operating Performance Point, or OPP. The ACPI specification refers to them as P-states, with P0 being the OPP with the highest frequency. Although an OPP is a combination of a frequency and a voltage, they are most often referred to by the frequency component alone.
### The CPUFreq driver
Linux has a component named CPUFreq that manages the transitions between OPPs. It is part of the board support for the package for each SoC. CPUFreq consists of drivers in drivers/cpufreq/, which make the transition from one OPP to another, and a set of governors that implement the policy of when to switch. It is controlled per-CPU via the /sys/devices/system/cpu/cpuN/cpufreq directory, with N being the CPU number. In there, we find a number of files, the most interesting of which are as follows:
- cpuinfo_cur_freq, cpuinfo_max_freq and cpuinfo_min_freq: The current frequency for this CPU, together with the maximum and minimum, measured in KHz.
- cpuinfo_transition_latency: The time, in nanoseconds, to switch from one OPP to another. If the value is unknown, it is set to -1.
- scaling_available_frequencies: A list of OPP frequencies available on this CPU.
- scaling_available_governors: A list of governors available on this CPU, which are described as follows:
  - scaling_governor: The CPUFreq governor currently being used.
  - scaling_max_freq and scaling_min_freq: The range of frequencies available to the governor in KHz.
  - scaling_setspeed: A file that allows you to manually set the frequency when the governor is userspace.
The governor sets the policy to change the OPP. It can set the frequency between the limits of scaling_min_freq and scaling_max_freq. The governors are named as follows:
- powersave: Always selects the lowest frequency.
- performance: Always selects the highest frequency.
- ondemand: Changes frequency based on the CPU utilization. If the CPU is idle less than 20% of the time, it sets the frequency to the maximum; if it is idle more than 30% of the time, it decrements the frequency by 5%.
- conservative: As ondemand, but switches to higher frequencies in 5% steps rather than going immediately to the maximum.
- userspace: Frequency is set by a user space program.
The parameters the ondemand governor uses to decide when to change OPP can be viewed and modified via /sys/devices/system/cpu/cpufreq/ondemand/. Both ondemand and conservative governors take into account the effort required to change frequency and voltage. This parameter is in cpuinfo_transition_latency. These calculations are for threads with a normal scheduling policy; if the thread is being scheduled in real-time, they will both immediately select the highest OPP so that the thread can meet its scheduling deadline.
The userspace governor allows the logic of selecting the OPP to be performed by a user space daemon. Examples include cpudyn and powernowd, although both are orientated toward x86-based laptops rather than embedded devices.

OPPs are coded in the device tree.
Eg:
cpu0_opp_table: opp-table {
  compatible = "operating-points-v2-ti-cpu";
  syscon = <&scm_conf>;

  opp50@300000000 {
    opp-hz = /bits/ 64 <300000000>;
    opp-microvolt = <950000 931000 969000>;
    opp-supported-hw = <0x06 0x0010>;
    opp-suspend;
  };
  opp100@600000000 {
    opp-hz = /bits/ 64 <600000000>;
    opp-microvolt = <1100000 1078000 1122000>;
    opp-supported-hw = <0x06 0x0040>;
  };

By selecting the user space governor, we can set the frequency by writing to scaling_setspeed, and so we can measure the power consumed at each OPP.

In most cases, the ondemand governor is the best one to use. To select a particular governor, you can either configure the kernel with a default governor, for example, CPU_FREQ_DEFAULT_GOV_ONDEMAND, or you can use a boot script to change the governor at boot time.

## Selecting the best idle state