# crosstool-ng

Crosstool-NG is a versatile (cross) toolchain generator. It supports many architectures and components and has a simple yet powerful menuconfig-style interface.

crosstool-NG aims at building toolchains.

Some pieces of the toolchain will eventually end up in the resulting binaries: static libraries are but an example.

Toolchains are made of different piece of software, each being quite complex and requiring specially crafted options to build and work seamlessly.

The toolchain sysroot is a directory which contains subdirectories for libraries, header files, and other configuration files.

subdirectories in sysroot:
lib: Contains the shared objects for the C library and the dynamic linker/loader, ld-linux
- usr/lib, the static library archive files for the C library, and any other libraries that may be installed subsequently
- usr/include: Contains the headers for all the libraries
- usr/bin: Contains the utility programs that run on the target, such as the ldd command
- use/share: Used for localization and internationalization
- sbin: Provides the ldconfig utility, used to optimize library loading paths

shared libraries and ld-linux - are needed on the target at runtime.

Components of the C library

It is composed of four main parts that together implement the POSIX API:

libc: The main C library that contains the well-known POSIX functions such as printf, open, close, read, write, and so on
- libm: Contains maths functions such as cos, exp, and log
- libpthread: Contains all the POSIX thread functions with names beginning with pthread_
- librt: Has the real-time extensions to POSIX, including shared memory and asynchronous I/O
The first one, libc, is always linked in but the others have to be explicitly linked with the -l option. The parameter to -l is the library name with lib stripped off.

You can verify which libraries have been linked in this or any other program by using the readelf command:
$ arm-cortex_a8-linux-gnueabihf-readelf -a myprog | grep "Shared library"
0x00000001 (NEEDED) Shared library: [libm.so.6]
0x00000001 (NEEDED) Shared library: [libc.so.6]

Shared libraries need a runtime linker, which you can expose using:
$ arm-cortex_a8-linux-gnueabihf-readelf -a myprog | grep "program interpreter"
[Requesting program interpreter: /lib/ld-linux-armhf.so.3]

### Linking with libraries

Static Linking

$ arm-cortex_a8-linux-gnueabihf-gcc -c test1.c
$ arm-cortex_a8-linux-gnueabihf-gcc -c test2.c
$ arm-cortex_a8-linux-gnueabihf-ar rc libtest.a test1.o test2.o
$ arm-cortex_a8-linux-gnueabihf-gcc helloworld.c -ltest \
-L../libs -I../libs -o helloworld

Dynamic Linking

$ arm-cortex_a8-linux-gnueabihf-gcc -fPIC -c test1.c
$ arm-cortex_a8-linux-gnueabihf-gcc -fPIC -c test2.c
$ arm-cortex_a8-linux-gnueabihf-gcc -shared -o libtest.so test1.o test2.o

arm-cortex_a8-linux-gnueabihf-gcc helloworld.c -ltest \
-L../libs -I../libs -o helloworld
For running the code, runtime linker must be present in target filesystem. It will look for libtest.so in /lib and /usr/lib

export LD_LIBRARY_PATH=/opt/lib:/opt/usr/lib

Library Version Numbers

Each library has a release version and an interface number. The release version is simply a string that is appended to the library name.

The soname encodes the interface number when the library was built and is used by the runtime linker when it loads the library. It is formatted as <library name>.so.<interface number>. For libjpeg.so.8.0.2, the soname is libjpeg.so.8.

It is possible to have two incompatible versions of the same library installed on the same system.

libjpeg.a: This is the library archive used for static linking
- libjpeg.so -> libjpeg.so.8.0.2: This is a symbolic link, used for dynamic linking
- libjpeg.so.8 -> libjpeg.so.8.0.2: This is a symbolic link, used when loading the library at runtime
- libjpeg.so.8.0.2: This is the actual shared library, used at both compile time and runtime

### Cross Compilation

some common build systems, including:
- Pure makefiles, where the toolchain is usually controlled by the make variable CROSS_COMPILE
- The GNU build system known as Autotools
- CMake

Autotools

The name Autotools refers to a group of tools that are used as the build system in many open source projects. The components are:
- GNU Autoconf
- GNU Automake
- GNU Libtool
- gnulib

Packages that use Autotools come with a script named configure that checks dependencies and generates makefiles according to what it finds. The configure script may also give you the opportunity to enable or disable certain features. You can find the options on offer by running ./configure –help.

$ ./configure
$ make
$ sudo make install

Autotools is able to handle cross development as well. You can influence the behavior of the configure script by setting these shell variables:
CC: The C compiler command
- CFLAGS: Additional C compiler flags
- LDFLAGS: Additional linker flags; for example, if you have libraries in a non-standard directory <lib dir>, you would add it to the library search path by adding -L<lib dir>
- LIBS: Contains a list of additional libraries to pass to the linker; for instance, -lm for the math library
- CPPFLAGS: Contains C/C++ preprocessor flags; for example, you would add -I<include dir> to search for headers in a non-standard directory <include dir>
- CPP: The C preprocessor to use

$ CC=arm-cortex_a8-linux-gnueabihf-gcc \
./configure –host=arm-cortex_a8-linux-gnueabihf

the default install directory is <sysroot>/usr/local/*. You would usually install it in <sysroot>/usr/*, so that the header files and libraries would be picked up from their default locations.