It is the part that starts the system up and loads the operating system kernel.

In an embedded Linux system, the bootloader has two main jobs: to initialize the system to a basic level and to load the kernel.

First, bootloader has to pass a pointer to a structure containing information about the hardware configuration, and second it has to pass a pointer to the kernel command line. The kernel command line is a text string that controls the behavior of Linux. Once the kernel has begun executing, the bootloader is no longer needed and all the memory it was using can be reclaimed.

A subsidiary job of the bootloader is to provide a maintenance mode for updating boot configurations, loading new boot images into memory, and, maybe, running diagnostics. This is usually controlled by a simple command-line user interface, commonly over a serial interface.

### Phase 1 – ROM code
The code that runs immediately after a reset or power-on has to be stored on-chip in the SoC; this is known as ROM code. It is loaded into the chip when it is manufactured, and hence the ROM code is proprietary and cannot be replaced by an open source equivalent.

it can only use Static Random Access Memory (SRAM), which does not require a memory controller.
Most embedded SoC designs have a small amount of SRAM on-chip, varying in size from as little as 4 KB to several hundred KB:
In SoCs where the SRAM is not large enough to load a full bootloader like U-Boot, there has to be an intermediate loader called the secondary program loader, or SPL.
At the end of the ROM code phase, the SPL is present in the SRAM and the ROM code jumps to the beginning of that code.

### Phase 2 – secondary program loader
The SPL must set up the memory controller and other essential parts of the system preparatory to loading the Tertiary Program Loader (TPL) into DRAM. The functionality of the SPL is limited by the size of the SRAM.

If the SPL has file system drivers built in, it can read well known file names, such as u-boot.img, from a disk partition.

The SPL usually doesn't allow for any user interaction, but it may print version information and progress messages, which you can see on the console.

### Phase 3 – TPL
Usually, there is a simple command-line user interface that lets you perform maintenance tasks, such as loading new boot and kernel images into flash storage, and loading and booting a kernel, and there is a way to load the kernel automatically without user intervention.

TPL loads kernel ( + optional FDT and initramfs ) into DRAM.

At the end of the third phase, there is a kernel in memory, waiting to be started.
Embedded bootloaders usually disappear from memory once the kernel is running, and perform no further part in the operation of the system.

Bootloader to Kernel

Bootloader passes following information to the kernel:

The machine number, which is used on PowerPC, and ARM platforms without support for a device tree, to identify the type of the SoC
- Basic details of the hardware detected so far, including at least the size and location of the physical RAM, and the CPU clock speed
- The kernel command line
- Optionally, the location and size of a device tree binary
- Optionally, the location and size of an initial RAM disk, called the initial RAM file system (initramfs)
The kernel command line is a plain ASCII string which controls the behavior of Linux

It is common to provide the root filesystem as a RAM disk, in which case it is the responsibility of the bootloader to load the RAM disk image into memory.

Device Tree

A device tree is a flexible way to define the hardware components of a computer system. Usually, the device tree is loaded by the bootloader and passed to the kernel, although it is possible to bundle the device tree with the kernel image itself to cater for bootloaders that are not capable of loading them separately.

The device tree represents a computer system as a collection of components joined together in a hierarchy, like a tree. The device tree begins with a root node, represented by a forward slash, /, which contains subsequent nodes representing the hardware of the system. Each node has a name and contains a number of properties in the form name = "value".

nodes have a compatible property. The Linux kernel uses this property to find a matching device driver by comparing it with the strings exported by each device driver in a structure of_device_id.

t is a convention that the value is composed of a manufacturer name and a component name, to reduce confusion between similar devices made by different manufacturers; hence, ti,am33xx and arm,cortex-a8. It is also quite common to have more than one value for the compatible property where there is more than one driver that can handle this device.

The CPU node and the memory node have a device_type property which describes the class of device. The node name is often derived from device_type.