## Exclusion locks

For most multi-threaded scenarios, often it can be observed that shared data is of custom sizes, for example, a structure with n elements of various types.
Concurrent code paths accessing such data usually comprise a bunch of instructions that are programmed to access and manipulate shared data;
such access operations must be executed atomically to prevent races. To ensure atomicity of such code blocks, mutual exclusion locks are used.

Most kernel data structures and other shared data elements such as shared buffers and device registers are protected from concurrent access through appropriate
exclusion-locking interfaces offered by the kernel.

### Spinlocks
Spinlocks are one of the simplest and lightweight mutual exclusion mechanisms widely implemented by most concurrent programming environments.
A spinlock implementation defines a lock structure and operations that manipulate the lock structure.
The lock structure primarily hosts an atomic lock counter among other elements, and operations interfaces include:
-An initializer routine, that initializes a spinlock instance to the default (unlock) state
-A lock routine, that attempts to acquire spinlock by altering the state of the lock counter atomically
-An unlock routine, that releases the spinlock by altering counter into unlock state

When a caller context attempts to acquire spinlock while it is locked (or held by another context), the lock function iteratively polls or spins for the lock
until available, causing the caller context to hog the CPU until lock is acquired.
It is therefore advised to ensure that code within critical sections is atomic or non-blocking, so that lock can be held for a short, deterministic duration.

Spinlocks are built around processor-specific atomic operations; the architecture branch of the kernel implements core spinlock operations (assembly programmed).
The kernel wraps the architecture-specific implementation through a generic platform-neutral interface that is directly usable by kernel service;

Generic spinlock interfaces can be found in the kernel header <linux/spinlock.h> while architecture-specific definitions are part of <asm/spinlock.h>.

The following code sample shows the usage of a basic spinlock interface:

DEFINE_SPINLOCK(s_lock);
spin_lock(&s_lock);
/* critical region ... */
spin_unlock(&s_lock);

Kernel code implements two variants of spinlock operations; one suitable for SMP platforms and the other for uniprocessor platforms.

<include/linux/spinlock.h> contains generic spinlock/rwlock declarations.

The generic kernel header <linux/spinlock.h> contains a conditional directive to decide on the appropriate (SMP or UP) API to pull.

The raw_spin_lock() and raw_spin_unlock() macros dynamically expand to the appropriate version of spinlock operations based on the type of platform (SMP or UP)
chosen in the build configuration.
For SMP platforms, raw_spin_lock() expands to the __raw_spin_lock() operation implemented in the kernel source file kernel/locking/spinlock.c.

### Alternate spinlock APIs
There might be scenarios where a specific shared resource or data might be accessed from both the process and interrupt context code of a kernel service.
The process context code needs to disable interrupts on the current processor while it takes the lock. This will ensure that an interrupt can never preempt the current context until the completion of the critical section and lock release.
Interrupts can still occur but are routed to other available CPUs, on which the interrupt handler can spin until lock becomes available. The spinlock interface provides an alternate locking routine spin_lock_irqsave(), which disables interrupts on the current processor along with kernel preemption.

local_irq_save() is invoked to disable hard interrupts for the current processor; notice how on failure to acquire the lock, interrupts are enabled by calling local_irq_restore(). Note that a lock taken by the caller using spin_lock_irqsave() needs to be unlocked using spin_lock_irqrestore(), which enables both kernel preemption and interrupts for the current processor before releasing lock.

Similar to hard interrupt handlers, it is also possible for soft interrupt context routines such as softirqs, tasklets, and other such bottom halves to contend for a lock held by the process context code on the same processor. This can be prevented by disabling the execution of bottom halves while acquiring lock in the process context. spin_lock_bh() is another variant of the locking routine that takes care of suspending the execution of interrupt context bottom halves on the local CPU.
local_bh_disable() suspends bottom half execution for the local CPU. To release a lock acquired by spin_lock_bh(), the caller context will need to invoke spin_unlock_bh(), which releases spinlock and BH lock for the local CPU.

Function	Description
spin_lock_init()	Initialize spinlock
spin_lock()	Acquire lock, spins on contention
spin_trylock()	Attempt to acquire lock, returns error on contention
spin_lock_bh()	Acquire lock by suspending BH routines on the local processor, spins on contention
spin_lock_irqsave()	Acquire lock by suspending interrupts on the local processor by saving current interrupt state, spins on contention
spin_lock_irq()	Acquire lock by suspending interrupts on the local processor, spins on contention
spin_unlock()	Release the lock
spin_unlock_bh()	Release lock and enable bottom half for the local processor
spin_unlock_irqrestore()	Release lock and restore local interrupts to previous state
spin_unlock_irq()	Release lock and restore interrupts for the local processor
spin_is_locked()	Return state of the lock, nonzero if lock is held or zero if lock is available

## Reader-writer spinlocks

Reader-writer locks enforce exclusion between reader and writer paths; this allows concurrent readers to share lock and a reader task will need to wait for the lock while a writer owns the lock. Rw-locks enforce standard exclusion between concurrent writers, which is desired.
Rw-locks are represented by struct rwlock_t declared in kernel header <linux/rwlock_types.h>

rwlocks can be initialized statically through the macro DEFINE_RWLOCK(v_rwlock) or dynamically at runtime throughrwlock_init(v_rwlock).
Reader code paths will need to invoke the read_lock routine.
read_lock(&v_rwlock);
/* critical section with read only access to shared data */
read_unlock(&v_rwlock);
Writer code paths use the following:
write_lock(&v_rwlock);
/* critical section for both read and write */
write_unlock(&v_lock);
Both read and write lock routines spin when lock is contended. The interface also offers non-spinning versions of lock functions called read_trylock() and write_trylock(). It also offers interrupt-disabling versions of the locking calls, which are handy when either the read or write path happens to execute in interrupt or bottom-half context.
Following is a summarized list of interface operations:
Function	Description
read_lock()	Standard read lock interface, spins on contention
read_trylock()	Attempts to acquire lock, returns error if lock is unavailable
read_lock_bh()	Attempts to acquire lock by suspending BH execution for the local CPU, spins on contention
read_lock_irqsave()	Attempts to acquire lock by suspending interrupts for the current CPU by saving current state of local interrupts, spins on contention
read_unlock()	Releases read lock
read_unlock_irqrestore()	Releases lock held and restores local interrupts to the previous state
read_unlock_bh()	Releases read lock and enables BH on the local processor
write_lock()	Standard write lock interface, spins on contention
write_trylock()	Attempts to acquire lock, returns error on contention
write_lock_bh()	Attempts to acquire write lock by suspending bottom halves for the local CPU, spins on contention
wrtie_lock_irqsave()	Attempts to acquire write lock by suspending interrupts for the local CPU by saving current state of local interrupts,. spins on contention
write_unlock()	Releases write lock
write_unlock_irqrestore()	Releases lock and restores local interrupts to the previous state
write_unlock_bh()	Releases write lock and enables BH on the local processor

## Mutex Locks

where a lock is held for longer, non-deterministic durations; sleeping locks are precisely designed to be engaged for such situations. Kernel mutexes are an implementation of sleeping locks: when a caller task attempts to acquire a mutex that is unavailable (already owned by another context), it is put into sleep and moved out into a wait queue, forcing a context switch allowing the CPU to run other productive tasks. When the mutex becomes available, the task in the wait queue is woken up and moved by the unlock path of the mutex, which can then attempt to lock the mutex.

Mutexes are represented by struct mutex, defined in include/linux/mutex.h and corresponding operations implemented in the source file kernel/locking/mutex.c.
In its basic form, each mutex contains a 64-bit atomic_long_t counter (owner), which is used both for holding lock state, and to store a reference to the task structure of the current task owning the lock. Each mutex contains a wait-queue (wait_list), and a spin lock(wait_lock) that serializes access to wait_list.
struct mutex {
        atomic_long_t owner;
        spinlock_t wait_lock;

        struct list_head wait_list;
};

The mutex API interface provides a set of macros and functions for initialization, lock, unlock, and to access the status of the mutex. These operation interfaces are defined in <include/linux/mutex.h>.
A mutex can be declared and initialized with the macro DEFINE_MUTEX(name).
There is also an option of initializing a valid mutex dynamically through mutex_init(mutex)
On contention, lock operations put the caller thread into sleep, which requires the caller thread to be put into TASK_INTERRUPTIBLE, TASK_UNINTERRUPTIBLE, or TASK_KILLABLE states, before moving it into the mutex wait list. To support this, the mutex implementation offers two variants of lock operations, one for uninterruptible and other for interruptible sleep.
Despite being possible blocking calls, mutex locking functions have been greatly optimized for performance. They are programmed to engage fast and slow path approaches while attempting lock acquisition.
The following code excerpt is of the mutex_lock() routine from <kernel/locking/mutex.c>:
void__sched mutex_lock(struct mutex* lock){might_sleep();if(!__mutex_trylock_fast(lock))__mutex_lock_slowpath(lock);}
Lock acquisition is first attempted by invoking a non-blocking fast path call __mutex_trylock_fast(). If it fails to acquire lock through due to contention, it enters slow path by invoking __mutex_lock_slowpath().

Conventionally, the concept of slow path has always been to put the caller task into sleep while waiting for the lock to become available. However, with the advent of many-core CPUs, there is a growing need for scalability and improved performance, so with an objective to achieve scalability, the mutex slow path implementation has been reworked with an optimization called optimistic spinning, a.k.a. midpath, which can improve performance considerably.
The core idea of optimistic spinning is to push contending tasks into poll or spin instead of sleep when the mutex owner is found to be running. Once the mutex becomes available (which is expected to be sooner, since the owner is found to be running) it is assumed that a spinning task could always acquire it quicker as compared to a suspended or sleeping task in the mutex wait list. However, such spinning is only a possibility when there are no other higher-priority tasks in ready state. With this feature, spinning tasks are more likely to be cache-hot, resulting in deterministic execution that yields noticeable performance improvement:
The __mutex_lock_common() function contains a slow path implementation with optimistic spinning; this routine is invoked by all sleep variants of mutex locking functions with appropriate flags as argument. This function first attempts to acquire mutex through optimistic spinning implemented through cancellable mcs spinlocks (osq field in mutex structure) associated with the mutex. When the caller task fails to acquire mutex with optimistic spinning, as a last resort this function switches to conventional slow path, resulting in the caller task to be put into sleep and queued into the mutex wait_list until woken up by the unlock path.

Debug checks and validatons on mutex
Incorrect use of mutex operations can cause deadlocks, failure of exclusion, and so on. To detect and prevent such possible occurrences, the mutex subsystem is equipped with appropriate checks or validations instrumented into mutex operations. These checks are by default disabled, and can be enabled by choosing the configuration optionCONFIG_DEBUG_MUTEXES=y during kernel build.
Following is a list of checks enforced by instrumented debug code:
- Mutex can be owned by one task at a given point in time
- Mutex can be released (unlocked) only by the valid owner, and an attempt to release mutex by a context that does not own the lock will fail
- Recursive locking or unlocking attempts will fail
- A mutex can only be initialized via the initializer call, and any attempt to memset mutex will never succeed
- A caller task may not exit with a mutex lock held
- Dynamic memory areas where held locks reside must not be freed
- A mutex can be initialized once, and any attempt to re-initialize an already initialized mutex will fail
- Mutexes may not be used in hard/soft interrupt context routines
The kernel lock validator infrastructure has been implemented to check and prove that none of the locking patterns observed during kernel runtime could ever cause deadlock. This infrastructure prints data pertaining to locking pattern such as:
- Point-of-acquire tracking, symbolic lookup of function names, and list of all locks held in the system
- Owner tracking
- Detection of self-recursing locks and printing out all relevant info
- Detection of lock inversion deadlocks and printing out all affected locks and tasks
The lock validator can be enabled by choosing CONFIG_PROVE_LOCKING=y during kernel build.

## Wait/Wound mutex

GPU buffers; these buffers are to be owned and accessed by various system entities such as GPU hardware, GPU driver, user-mode applications, and other video-related drivers. User mode contexts can submit the dma buffers for processing in an arbitrary order, and the GPU hardware may process them at arbitrary times. If locking is used to control the ownership of the buffers, and if multiple buffers must be manipulated at the same time, deadlocks cannot be avoided. Wait/wound mutexes are designed to facilitate dynamic ordering of nested locks, without causing lock-inversion deadlocks. This is achieved by forcing the context in contention to wound, meaning forcing it to release the holding lock.

Scenario:
Thread T1 Thread T2
=========== ==========
lock(bufA); lock(bufB);
lock(bufB); lock(bufA);
 .... ....
 .... ....
unlock(bufB); unlock(bufA);
unlock(bufA); unlock(bufB);
Execution of T1 and T2 concurrently might result in each thread waiting for the lock held by the other, causing deadlock. Wait/wound mutex prevents this by letting the thread that grabbed the lock first to remain in sleep, waiting for nested lock to be available. The other thread is wound, causing it to release its holding lock and start over again. Suppose T1 got to lock on bufA before T2 could acquire lock on bufB. T1 would be considered as the thread that got there first and is put to sleep for lock on bufB, and T2 would be wound, causing it to release lock on bufB and start all over. This avoids deadlock and T2 would start all over when T1 releases locks held.
Wait/wound mutexes are represented through struct ww_mutex defined in the header <linux/ww_mutex.h>

The first step to use wait/wound mutex is to define a class, which is a mechanism to represent a group of locks. When concurrent tasks contend for the same locks, they must do so by specifying this class.
A class can be defined using a macro:
static DEFINE_WW_CLASS(bufclass);
Each class declared is an instance of type struct ww_class and contains an atomic counter stamp, which is used to hold a sequence number that records which one of the contending tasks got there first. Other fields are used by the kernel's lock validator to verify correct usage of the wait/wound mechanism.
Each contending thread must invoke ww_acquire_init() before attempting nested locking calls. This sets up the context by assigning a sequence number to track locks.
Once the context is set up and initialized, tasks can begin acquiring locks with either ww_mutex_lock() or ww_mutex_lock_interruptible() calls:
When a task grabs all nested locks (using any of these locking routines) associated with a class, it needs to notify acquisition of ownership using the function ww_acquire_done(). This call marks the end of the acquisition phase, and the task can proceed to process shared data:
When a task completes its processing of shared data, it can begin releasing all of the locks held, with calls to the ww_mutex_unlock() routine. Once all of the locks are released, the context must be released with a call to ww_acquire_fini().

ww_acquire_init ----> ww_mutex_lock ----> ww_acquire_done ----> ww_mutex_unlock ----> ww_acquire_fini.

## Semaphores
A typical semaphore implementation comprises a counter, wait queue, and set of operations that can increment/decrement the counter atomically.

When a semaphore is used to protect a shared resource, its counter is initialized to a number greater than zero, which is considered to be unlocked state. A task seeking access to a shared resource begins by invoking the decrement operation on the semaphore. This call checks the semaphore counter; if it is found to be greater than zero, the counter is decremented and the function returns success. However, if the counter is found to be zero, the decrement operation puts the caller task to sleep until the counter is found to have increased to a number greater than zero.
Semaphore structure and its interface operations are declared in the kernel header <include/linux/semaphore.h>:
semaphore operations (inc/dec) are programmed to acquire lock before manipulating count. wait_list is used to queue tasks to sleep while they wait for the semaphore count to increase beyond zero.

Semaphores can be declared and initialized to 1 through a macro: DEFINE_SEMAPHORE(s).
A semaphore can also be initialized dynamically to any positive number through the following:
void sema_init(structsemaphore*sem,intval)
Following is a list of operation interfaces with a brief description of each. Routines with naming convention down_xxx() attempt to decrement the semaphore, and are possible blocking calls (except down_trylock()), while routine up() increments the semaphore and always succeeds:
/** * down_interruptible - acquire the semaphore unless interrupted * @sem: the semaphore to be acquired * * Attempts to acquire the semaphore. If no more tasks are allowed to * acquire the semaphore, calling this function will put the task to sleep. * If the sleep is interrupted by a signal, this function will return -EINTR. * If the semaphore is successfully acquired, this function returns 0. */
int down_interruptible(structsemaphore*sem);

/** * down_killable - acquire the semaphore unless killed * @sem: the semaphore to be acquired * * Attempts to acquire the semaphore. If no more tasks are allowed to * acquire the semaphore, calling this function will put the task to sleep. * If the sleep is interrupted by a fatal signal, this function will return * -EINTR. If the semaphore is successfully acquired, this function returns * 0. */
int down_killable(structsemaphore*sem);

/** * down_trylock - try to acquire the semaphore, without waiting * @sem: the semaphore to be acquired * * Try to acquire the semaphore atomically. Returns 0 if the semaphore has * been acquired successfully or 1 if it it cannot be acquired. * */
int down_trylock(structsemaphore*sem);

/** * down_timeout - acquire the semaphore within a specified time * @sem: the semaphore to be acquired * @timeout: how long to wait before failing * * Attempts to acquire the semaphore. If no more tasks are allowed to * acquire the semaphore, calling this function will put the task to sleep. * If the semaphore is not released within the specified number of jiffies, * this function returns -ETIME. It returns 0 if the semaphore was acquired. */
int down_timeout(structsemaphore*sem,longtimeout);

/** * up - release the semaphore * @sem: the semaphore to release * * Release the semaphore. Unlike mutexes, up() may be called from any * context and even by tasks which have never called down(). */
void up(structsemaphore*sem);

#### Reader-writer semaphores
This interface is an implementation of sleeping reader-writer exclusion, which serves as an alternative for spinning ones. Reader-writer semaphores are represented by struct rw_semaphore, declared in the kernel header <linux/rwsem.h>:
This structure is identical to that of a mutex, and is designed to support optimistic spinning with osq; it also includes debug support through the kernel's lockdep. Count serves as an exclusion counter, which is set to 1, allowing a maximum of one writer to own the lock at a point in time.
An rw_semaphore can be instantiated and initialized statically through DECLARE_RWSEM(name), and alternatively, it can be dynamically initialized throughinit_rwsem(sem).
As with the case of rw-spinlocks, this interface too offers distinct routines for lock acquisition in reader and writer paths. Following is a list of interface operations:
/* reader interfaces */
   void down_read(struct rw_semaphore*sem);
void up_read(struct rw_semaphore*sem);

/* trylock for reading -- returns 1 if successful, 0 if contention */
int down_read_trylock(struct rw_semaphore*sem);
void up_read(struct rw_semaphore*sem);

/* writer Interfaces */
   void down_write(struct rw_semaphore*sem);
int __must_check down_write_killable(struct rw_semaphore*sem);

/* trylock for writing -- returns 1 if successful, 0 if contention */
int down_write_trylock(struct rw_semaphore*sem);
   void up_write(struct rw_semaphore*sem);/* downgrade write lock to read lock */
   void downgrade_write(struct rw_semaphore*sem);

/* check if rw-sem is currently locked */
   int rwsem_is_locked(struct rw_semaphore*sem);
These operations are implemented in the source file <kernel/locking/rwsem.c>

### Sequence Locks
sequential lock aims at providing a quick and lock-free access to shared resources. Sequential locks are best when the resource that needs to be protected is small and simple, with write access being quick and non-frequent, as internally sequential locks fall back on the spinlock primitive.

Sequential locks introduce a special counter that is incremented every time a writer acquires a sequential lock along with a spinlock. After the writer completes, it releases the spinlock and increments the counter again and opens the access for other writers. For read, there are two types of readers: sequence readers and locking readers. The sequence reader checks for the counter before it enters the critical section and then checks again at the end of it without blocking any writer. If the counter remains the same, it implies that no writer had accessed the section during read, but if there is an increment of the counter at the end of the section, it is an indication that a writer had accessed, which calls for the reader to re-read the critical section for updated data. A locking reader, as the name implies, will get a lock and block other readers and writers when it is in progress; it will also wait when another locking reader or writer is in progress.
A sequence lock is represented by the following type:
typedefstruct{structseqcountseqcount;spinlock_tlock;}seqlock_t;
We can initialize a sequence lock statically using the following macro:
#define DEFINE_SEQLOCK(x) \
        seqlock_t x = __SEQLOCK_UNLOCKED(x)
Actual initialization is done using the __SEQLOCK_UNLOCKED(x)

To dynamically initialize sequence lock, we need to use the seqlock_init macro.
Linux provides many APIs for using sequence locks, which are defined in </linux/seqlock.h>

### Completion Locks
Completion locks are an efficient way to achieve code synchronization if you need one or multiple threads of execution to wait for completion of some event, such as waiting for another process to reach a point or state. Completion locks may be preferred over a semaphore for a couple of reasons: multiple threads of execution can wait for a completion, and using complete_all(), they can all be released at once.

Completion can be used by including <linux/completion.h> and by creating a variable of type struct completion, which is an opaque structure for maintaining the state of completion. It uses a FIFO to queue the threads waiting for the completion event:
Completion basically consists of initializing the completion structure, waiting through any of the variants of wait_for_completion() call, and finally signalling the completion through complete() or the complete_all() call. There are also functions to check the state of completions during its lifetime.
The following macro can be used for static declaration and initialization of a completion structure:
#define DECLARE_COMPLETION(work) \ struct completion work = COMPLETION_INITIALIZER(work)
The following inline function will initialize a dynamically created completion structure:
static inline void init_completion(struct completion* x)
{x->done=0;
init_waitqueue_head(&x->wait);}
The following inline function will be used to reinitialize a completion structure if you need to reuse it. This can be used after complete_all():
static inline void reinit_completion(struct completion* x)
{x->done=0;}
If any thread needs to wait for a task to complete, it will call wait_for_completion() on the initialized completion structure. If the wait_for_completion operation happens after the call to complete() or complete_all(), the thread simply continues, as the reason it wanted to wait for has been satisfied; else, it waits till complete() is signalled.

The execution thread that wants to signal the completion of the intended task calls complete() to a waiting thread so that it can continue. Threads will be awakened in the same order in which they were queued. In the case of multiple waiters, it calls complete_all():