mmap()

void *mmap(void *addr, size_t length, int prot, int flags,
        int fd, off_t offset);

This function maps length bytes of memory from the file with the descriptor fd, starting at offset in the file, and returns a pointer to the mapping, assuming it is successful. Since the underlying hardware works in pages, length is rounded up to the nearest whole number of pages. The protection parameter, prot, is a combination of read, write, and execute permissions and the flags parameter contains at least MAP_SHARED or MAP_PRIVATE.

man page
------------
mmap() creates a new mapping in the virtual address space of the calling process. The starting address for the new mapping is specified in
       addr. The length argument specifies the length of the mapping (which must be greater than 0).

       If addr is NULL, then the kernel chooses the (page-aligned) address at which to create the mapping; this is the most portable method of
       creating a new mapping. If addr is not NULL, then the kernel takes it as a hint about where to place the mapping; on Linux, the kernel
       will pick a nearby page boundary (but always above or equal to the value specified by /proc/sys/vm/mmap_min_addr) and attempt to create the
       mapping there. If another mapping already exists there, the kernel picks a new address that may or may not depend on the hint.

The address of the new mapping is returned as the result of the call.

       The contents of a file mapping (as opposed to an anonymous mapping; see MAP_ANONYMOUS below), are initialized using length bytes starting
       at offset offset in the file (or other object) referred to by the file descriptor fd. offset must be a multiple of the page size as re‐
       turned by sysconf(_SC_PAGE_SIZE).

       After the mmap() call has returned, the file descriptor, fd, can be closed immediately without invalidating the mapping.

       The prot argument describes the desired memory protection of the mapping (and must not conflict with the open mode of the file). It is ei‐
       ther PROT_NONE or the bitwise OR of one or more of the following flags:

       PROT_EXEC Pages may be executed.

       PROT_READ Pages may be read.

       PROT_WRITE Pages may be written.

       PROT_NONE Pages may not be accessed.

       The flags argument determines whether updates to the mapping are visible to other processes mapping the same region, and whether updates
       are carried through to the underlying file. This behavior is determined by including exactly one of the following values in flags:

      MAP_SHARED
        Share this mapping. Updates to the mapping are visible to other processes mapping the same region, and (in the case of file-backed
        mappings) are carried through to the underlying file. (To precisely control when updates are carried through to the underlying file
        requires the use of msync(2).)

       MAP_SHARED_VALIDATE (since Linux 4.15)
        This flag provides the same behavior as MAP_SHARED except that MAP_SHARED mappings ignore unknown flags in flags. By contrast, when
        creating a mapping using MAP_SHARED_VALIDATE, the kernel verifies all passed flags are known and fails the mapping with the error
        EOPNOTSUPP for unknown flags. This mapping type is also required to be able to use some mapping flags (e.g., MAP_SYNC).

       MAP_PRIVATE
        Create a private copy-on-write mapping. Updates to the mapping are not visible to other processes mapping the same file, and are
        not carried through to the underlying file. It is unspecified whether changes made to the file after the mmap() call are visible in
        the mapped region.

       Both MAP_SHARED and MAP_PRIVATE are described in POSIX.1-2001 and POSIX.1-2008. MAP_SHARED_VALIDATE is a Linux extension.

       In addition, zero or more of the following values can be ORed in flags:

       MAP_32BIT (since Linux 2.4.20, 2.6)
        Put the mapping into the first 2 Gigabytes of the process address space. This flag is supported only on x86-64, for 64-bit pro‐
        grams. It was added to allow thread stacks to be allocated somewhere in the first 2 GB of memory, so as to improve context-switch
        performance on some early 64-bit processors. Modern x86-64 processors no longer have this performance problem, so use of this flag
        is not required on those systems. The MAP_32BIT flag is ignored when MAP_FIXED is set.

       MAP_ANON
        Synonym for MAP_ANONYMOUS. Deprecated.

       MAP_ANONYMOUS
        The mapping is not backed by any file; its contents are initialized to zero. The fd argument is ignored; however, some implementa‐
        tions require fd to be -1 if MAP_ANONYMOUS (or MAP_ANON) is specified, and portable applications should ensure this. The offset ar‐
        gument should be zero. The use of MAP_ANONYMOUS in conjunction with MAP_SHARED is supported on Linux only since kernel 2.4.
[...]

   munmap()
       The munmap() system call deletes the mappings for the specified address range, and causes further references to addresses within the range
       to generate invalid memory references. The region is also automatically unmapped when the process is terminated. On the other hand, clos‐
       ing the file descriptor does not unmap the region.

       The address addr must be a multiple of the page size (but length need not be). All pages containing a part of the indicated range are un‐
       mapped, and subsequent references to these pages will generate SIGSEGV. It is not an error if the indicated range does not contain any
       mapped pages.

RETURN VALUE
       On success, mmap() returns a pointer to the mapped area. On error, the value MAP_FAILED (that is, (void *) -1) is returned, and errno is
       set to indicate the cause of the error.

       On success, munmap() returns 0. On failure, it returns -1, and errno is set to indicate the cause of the error (probably to EINVAL).

Uses

1) You can use mmap to allocate an area of private memory by setting MAP_ANONYMOUS in the flags parameter and setting the file descriptor fd to -1. This is similar to allocating memory from the heap using malloc, except that the memory is page-aligned and in multiples of pages. The memory is allocated in the same area as that used for libraries. In fact, this area is referred to by some as the mmap area for this reason.
Anonymous mappings are better for large allocations because they do not pin down the heap with chunks of memory, which would make fragmentation more likely.

malloc (in glibc at least) stops allocating memory from the heap for requests over 128 KiB and uses mmap in this way, so in most cases, just using malloc is the right thing to do.

2) It is possible for a driver to allow its device node to be mmaped and share some of the device memory with an application.